## Slide 1
CHATBOT
Vjti Chatbot
Puru Brahmankar
Pratik Bhalekar
Electrical Engineering Department | VJTI, Mumbai

## Slide 2
Problem Statement
Urban mobility in India faces traffic congestion, rising carbon emissions, and inefficient short-distance transport — existing solutions are costly, unsustainable, or not optimised for compact urban navigation.
DUPAHIYA aims to design a two-wheeled horizontal self-balancing personal transporter promoting sustainable and efficient urban mobility.
Three control strategies are implemented and compared: PID, LQR, and Fuzzy Logic Control (FLC) — evaluating stability, responsiveness, and energy efficiency.
"Made in India" approach — cost-effective, locally manufacturable, reducing dependency on imported technologies.
🚗
Traffic
Congestion
🌿
Carbon
Emissions
⚙️
No Indigenous
Platform

## Slide 3
Research Plan
01
Electronic Design
& Power Architecture
Power management & voltage regulation for high-torque BLDC motors
ESC design with high-frequency PWM switching + regenerative braking
9-axis IMU sensor fusion with Kalman filters for clean tilt data
02
Modelling &
Control Algorithms
State-space mathematical modelling (inverted pendulum)
PID — error correction loops
LQR — optimal multi-variable state-feedback
Fuzzy Logic — handles non-linearities & load variation
03
Testing &
Efficiency Analysis
Settling time & steady-state error across control schemes
Current draw monitoring — stationary vs active transit
"Cost of transport" benchmarking for battery range optimisation

## Slide 4
Development Progress
Step 1
Hardware Reverse Engineering & Modification
Decommissioned stock Segway motherboard → direct BLDC hub motor interface. Integrated 2× JYQD v7.3e2 ESCs with Hall Sensor feedback. Teensy 4.1 deployed as primary flight controller for high-frequency loops.
Step 2
Sensing & State Estimation
IMU 9250 (9-DOF) interfaced via I²C for real-time orientation. Sensor fusion implemented to extract stable Pitch & Roll data, filtering mechanical vibrations and centrifugal accelerations.
Step 3
Control System Implementation (PID)
Custom PID algorithm translates angular error → motor PWM commands. P: immediate tilt response | I: corrects steady-state lean | D: dampens oscillations. Loop optimised to 100–200 Hz for real-time responsiveness.

## Slide 5
Next Stage & Key Focus
1
Real-Time Balancing (Closed-Loop)
Sensor fusion → pitch angle extraction → error vs 0° setpoint → PWM correction. High-speed loop ensures instantaneous motor response.
2
Full Control Algorithm Comparison
PID (baseline) vs LQR (optimal state-feedback) vs Fuzzy Logic (non-linearity handling). Metrics: settling time, steady-state error, energy consumption.
3
PID Tuning & Diagnostics
High Kp → shaking | Low Kp → sluggish | Missing Kd → overshoot | Required Ki → eliminates steady-state drift. Systematic bench testing for optimal gain set.
Research
Focus
Compare LQR & Fuzzy Logic vs standard PID Determine optimal balance between: ✦ Computational overhead ✦ Battery longevity ✦ Stability performance
Target: Indigenous low-cost platform ready for real-world deployment